## Slide 1
HACKFUSION 2026 · IEEE ROBOTICS & AUTOMATION SOCIETY · THEME 3
GARUDA
A physics-informed digital twin that monitors a drone's health in real-time, predicts failures before they happen, and makes autonomous safety decisions it can explain.
7
PHYSICS MODELS
6
DECISION TIERS
7
KALMAN FILTERS
5
FAILURE DEMOS
Team GarudaOne

## Slide 2
THE PROBLEM
Drones don't understand their own physics
A drone in turbulent wind burns more power. A hot battery loses capacity. A worn motor creates asymmetric thrust. Today's drones don't track any of this — they find out when they crash.
No energy awareness
Battery drains unpredictably under wind load. The drone doesn't know it can't make it home until it's already too late.
Blind to atmosphere
Air density drops at altitude, turbulence varies with terrain, temperature affects everything. None of this is modeled.
No component health
Motor bearings wear, batteries heat up, propellers degrade. No way to detect partial failure before it becomes total.
We need a system that continuously estimates the drone's physical state, predicts failures, quantifies how certain it is, and makes safety decisions it can justify.

## Slide 3
OUR APPROACH
Five physics modules running in a loop at 10 Hz
Each module feeds into the next. The decision engine evaluates the complete picture every 100 ms.
MODULE | WHAT IT DOES | PHYSICS BASIS
Environment Model | Simulates wind, air density, temperature, pressure, turbulence as a function of altitude and time | ICAO ISA + Dryden (O-U)
Vehicle Health | Tracks battery temperature, charge state, per-motor efficiency, payload mass, structural G-stress | Thermal ODE + Coulomb
Energy Forecasting | Predicts power consumption, remaining flight time, mission feasibility | Actuator Disk Theory
State Estimator | Fuses physics predictions with noisy sensors. 95% confidence intervals on every state | 7× Kalman filters
Decision Engine | Decides: continue, slow down, change altitude, return home, or abort | 6-tier hierarchical rules

## Slide 4
ARCHITECTURE
How the pieces fit together
┌──────────────────────────────────────────────────────────────────┐ │ DASHBOARD (Rich TUI — 6 panels, 10 Hz refresh) │ │ Telemetry · Environment · Health · Energy · Uncertainty · AI │ └───────────────────────────────┬──────────────────────────────────┘ │ JSON telemetry snapshots ┌───────────────────────────────┴──────────────────────────────────┐ │ DIGITAL TWIN ENGINE (Python, 10 Hz main loop) │ │ │ │ ┌───────────────┐ ┌────────────────┐ ┌────────────────────────┐ │ │ │ Environment │ │ Vehicle Health │ │ Energy & Endurance │ │ │ │ ISA + Dryden │ │ Battery ODE │ │ Actuator Disk Theory │ │ │ └───────┬───────┘ └───────┬────────┘ └──────────┬─────────────┘ │ │ └─────────────────┼─────────────────────┘ │ │ ┌──────┴──────┐ │ │ │ Kalman │ 7 state filters │ │ │ Filter UQ │ 95% confidence bounds │ │ └──────┬──────┘ │ │ ┌──────┴──────┐ │ │ │ DECISION │ 6-tier hierarchical engine │ │ │ ENGINE │ + evidence trail logger │ │ └─────────────┘ │ └───────────────────────────────────────────────────────────────────┘ │ autonomous commands ┌───────────────────────────────┴──────────────────────────────────┐ │ FLIGHT LAYER PX4 via MAVSDK · Voice ("Hey Garuda") · LFM AI │ └──────────────────────────────────────────────────────────────────┘
Fully async Python. Event-bus decoupled modules. 14 drone states with enforced transitions. Real hardware parameters from our 249g prototype.

## Slide 5
PHYSICS MODELS
Environment: atmosphere + wind
ICAO Standard Atmosphere
T(h) = 288.15 − 0.0065 · h
ρ(h) = 1.225 · (T / 288.15)^4.256
Air density drops with altitude — directly affects how much power the motors need to produce the same thrust. Recalculated every tick.
Dryden Wind Turbulence (MIL-F-8785C)
x(t+dt) = x(t)·exp(−dt/τ) + σ·√(1−exp(−2dt/τ))·N(0,1)
Wind is random but correlated in time (τ=4s). Standard aerospace model. Vertical axis has 60% lower turbulence than horizontal.
Disturbances we inject live
Crosswind gust: 12 m/s sudden lateral wind
Temperature spike: +20°C (flying over a heat island)
Downdraft: 5 m/s vertical shear (microburst)
Wind shear layer: Altitude-dependent velocity gradient
Each disturbance is a single function call. The decision engine reacts within the same tick.

## Slide 6
PHYSICS MODELS
Vehicle health + energy forecasting
Battery: thermal ODE + Coulomb counting
dT/dt = (I²R − h·A·ΔT) / (m·Cp)
Battery heats from internal resistance (I²R) and cools from airflow. LiPo capacity drops with temperature — a hot battery gives you less flight time than voltage suggests. Real 3S/450mAh pack params.
Motor degradation
4 motors tracked independently. Bearing wear at 15%/1000h. Delta between best and worst motor (imbalance) is a key safety signal.
Power: Actuator Disk Momentum Theory
P_hover = √(T³ / 2ρA) · κ / η
P_fwd = P_hover·f(v) + ½ρCdAv³
Hover power depends on thrust, air density, disk area (4× 2-inch props), and rotor efficiency. Forward flight adds parasitic drag. All from real hardware config.
Safe operating envelope (dynamic)
• Max altitude (density-limited)
• Max speed (rotor-efficiency-limited)
• Max range at cruise speed
• Can we reach target, return home, and keep 30s reserve?

## Slide 7
UNCERTAINTY QUANTIFICATION
Kalman filter: physics meets sensors
Physics models predict what should happen. Sensors measure what actually happened. The Kalman filter finds the best estimate and tells you how confident it is.
Predict (from physics model): x̂ = model_prediction(alt, speed, wind) P += Q · dt ← uncertainty grows Update (from noisy sensor): K = P / (P + R) ← Kalman gain x̂ += K · (z − x̂) ← fuse measurement P = (1 − K) · P ← uncertainty shrinks Output: estimate ± 2σ ← 95% confidence band
7 independent filters tracking:
STATE | SENSOR NOISE (σ)
Position N, E | GPS: 0.25 m
Altitude | Barometer: 0.25 m
Airspeed | Pitot: 0.20 m/s
Wind speed | Inferred: 0.40 m/s
Battery SoC | Current sensor: 0.30%
Endurance | Derived: ±25 s
The decision engine uses uncertainty to calibrate how aggressive its responses are.

## Slide 8
AUTONOMOUS DECISIONS
6-tier hierarchical safety engine
Evaluates from most severe to least. Stops at the first tier that triggers. Every decision carries an evidence trail.
ABORT
Emergency landing — immediate
Battery ≥ 60°C · rotor eff < 30% · structural stress exceeded · endurance < 45s
RTB
Return to base
Not enough energy for RTH · SoC ≤ 18% · battery ≥ 50°C · motor degradation · wind ≥ 8.5 m/s
ALT
Change altitude
Air density too thin at current height · vertical downdraft ≥ 3 m/s
SLOW
Reduce speed
Turbulence intensity ≥ 0.50 · crosswind ≥ 5.5 m/s · rotor imbalance ≥ 0.15
ROUTE
Modify trajectory
Headwind ≥ 60% of airspeed — reroute to save energy
GO
Continue mission
All parameters nominal. Confidence: 96%.
Every decision record includes: trigger parameter + value + threshold, confidence score, physics snapshot, and alternatives considered but rejected.

## Slide 9
DEMONSTRATION
5 failure scenarios, tested live
We inject each disturbance during the simulation and show the decision engine reacting in real-time with evidence.
# | SCENARIO | DECISION
1 | 12 m/s crosswind gust | REDUCE SPEED
2 | Motor #3 bearing failure (35%) | SLOW → RTB
3 | Battery overheating (58°C) | ABORT
4 | Payload released mid-flight | CONTINUE (re-calc)
5 | Downdraft + thin air + low battery | ALTER ALT → RTB
Evidence trail (actual output)
{ "decision": "RETURN_TO_BASE", "confidence": 0.92, "triggers": [{ "parameter": "battery_soc", "value": 16.2, "threshold": 18.0, "severity": "WARNING" }], "reason": "Energy reserve insufficient for safe RTH.", "physics_snapshot": { "wind_speed": 7.3, "hover_power": 28.4, "rotor_effs": [.89,.88,.58,.90] } }

## Slide 10
INNOVATION BEYOND THE BRIEF
"Hey Garuda" — voice-controlled digital twin
Fully offline voice pipeline. No cloud, no internet — everything on-device. Think Siri, but for a drone.
Voice pipeline
1
Wake word — openWakeWord listens for "Garuda" (3-8% CPU)
2
Speech-to-text — Whisper Tiny (INT8, 39 MB)
3
Intent routing — keyword (<5ms), Needle 26M (<20ms), LFM (200ms)
4
Voice feedback — Piper TTS: "Starting orbit mode"
Most commands resolve in under 20 ms.
AI models on a Raspberry Pi 5
MODEL | SIZE | SPEED
LFM-2.5-230M (Liquid AI brain) | 180 MB | 42 tok/s
Needle 26M (fast router) | 14 MB | 1,200 tok/s
PicoDet-S (object detection) | 4 MB | 50 FPS
Whisper Tiny (speech-to-text) | 39 MB | Real-time
Piper TTS (text-to-speech) | 20 MB | Real-time
All CPU-only on RPi 5 (8 GB). No GPU. Drone weighs 249g.

## Slide 11
DASHBOARD
6 panels, all updating at 10 Hz
Built with Python's Rich library. Reads telemetry JSON from the twin runner.
Telemetry
Altitude, airspeed, heading, GPS, distance to target/home
Environment
ISA density, temperature, pressure, wind vector, turbulence
Vehicle Health
Battery SoC + temp, 4× motor bars, structural stress
Energy
Power draw, hover/cruise power, endurance countdown, envelope
Uncertainty
Every Kalman estimate with ±2σ confidence bounds
Decision
Current action, confidence %, trigger reason, alternatives
During the demo we inject failure scenarios live and watch all 6 panels react. The decision panel shows exactly why the engine made its choice.

## Slide 12
COVERAGE
How we address each judging criterion
CRITERION | OUR IMPLEMENTATION
Physical-state estimation accuracy | 7 Kalman filters fusing ISA physics with sensors. Each state has 95% CI bounds.
Environmental modeling quality | ICAO atmosphere + Dryden wind turbulence (O-U process) + 4 injectable disturbances.
Energy/endurance prediction | Actuator disk power with real hardware params. Mission feasibility: target + RTH + 30s reserve.
Safety decision effectiveness | 6-tier engine with confidence scores. Evidence trail for every decision. 5 failure scenarios.
Robustness under changing conditions | Crosswind, motor failure, thermal runaway, payload change, combined — all real-time.
Physics/ML integration | Kalman = physics+sensors. CfC LNN = learned control. LFM = NL understanding. Voice = ML chain.
Innovation | Voice-controlled twin, Liquid AI, evidence audit trails, real sub-250g hardware parameters.

## Slide 13
WHAT'S NEXT
Future development
The modular architecture means each piece can be upgraded independently.
Voice biometrics
Owner + 2 registered voices only. Speaker verification rejects unauthorized commands.
Satellite connectivity
Iridium/Starlink backhaul for beyond-line-of-sight. Cloud twin mirroring.
Multi-drone swarm
PX4 multi-SITL already configured. Coordinated formation flying.
Edge SLAM
OpenVINS / ORB-SLAM3 via VisionPoseSource interface. Already defined.
RL decision refinement
Flight data tunes thresholds via RL. Physics constraints stay, RL tunes margins.

## Slide 14
GARUDA
It doesn't just simulate the drone. It understands the physics.
Real equations. Real hardware parameters. Real-time decisions with evidence you can audit.
7
PHYSICS MODELS
6
SAFETY TIERS
7
KALMAN FILTERS
5
LIVE SCENARIOS
<20ms
VOICE LATENCY
Team GarudaOne · HackFusion 2026 · IEEE RAS
"Hey Garuda, take off."